# 4 – Worksheets

# Worksheet 4-1: Energy data

Company: Cheers Beers Ltd	Responsible: Mister XY		Page: 1

Reference values:	Product:	250 000 hl	Heated area:

Mileage: 	1 500 000 km	..........................:

| No. | Energy | Annual consumption | Unit | Spec. costs | Conversion into kWh | Consumption in kWh | Share in % | Specific consumption | Unit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Electricity | 2 480 000 | kWh | 0.10 |  | 2 480 000 | 20% | 9.92 | kWh/hl |
|  | Peak load | 572 | kW | 135.00 |  |  |  |  |  |
| 2 | District heating |  | GJ |  | x 277.8 |  |  |  |  |
|  | Peak load |  | kW |  |  |  |  |  |  |
| 3 | Oil | 700 000 | kg | 0.50 | x 11.4 | 7 980 000 | 64% | 31.92 2.80 | kWh/hl kg/hl |
| 4 | Gas |  | Nm³ |  | x 10.0 |  |  |  |  |
| 5 | ………… |  |  |  |  |  |  |  |  |
| 6 | …………. |  |  |  |  |  |  |  |  |
| 7 | ……….… |  |  |  |  |  |  |  |  |
| 8 | Fuels: Diesel | 200 000 | litre | 0.80 | x 10.0 | 2 000 000 | 16% | 13.33 | l/100 km |
| 9 | Gasoline |  | litre |  | x 9.0 |  |  |  |  |
| 10 | …………. |  |  |  |  |  |  |  |  |
|  | Total |  |  |  |  | 12 460 000 | 100% | 835 200 | 100% |

Worksheet 4-2: Meters and measuring instruments

Company: Cheers Beers Ltd

| Energy flow measured | Type of measurement and place | Meter no. | Current recording frequency | Recorded by: | Future recording frequency |
| --- | --- | --- | --- | --- | --- |
| Oil steam generator 1 | Oil flow meter at steam generator | Oil-1 | Daily | Mr. Steam | Daily |
| Oil hot water generator | Level indicator at tank and records of filling amount | - | Annually | Mr. Steam | Monthly |
| Electricity mash house | Online recording from process control unit | 188800025 | Daily | Mr. Steam | Daily |
| Electricity brewing house | Online recording from process control unit | 188800029 | Daily | Mr. Steam | Daily |
| Electricity storage and fermentation | Online recording from process control unit | 188800035 | Daily | Mr. Steam | Daily |
| Electricity filling line | Online recording from process control unit | 188800036 | Daily | Mr. Steam | Daily |
| Electricity administration | Reading the meter in the cellar | 188800022 | Annually | In future: Mr. Steam | Monthly |
|  | And additional 12 submeters! |  |  |  |  |
| Diesel | Bills from nearby petrol station | - | Irregular | In future: Mr. Steam | Monthly |

Worksheet 4-3: Conversion units and heat consumers

Company: Cheers Beers Ltd	Period: 2002

|  | No. | Name | Energy carrier | Power (kWthermal) | Consumption in kg | Operating hours per year | Parameter (p,T) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Heat | 1 | Steam generator 1 | Oil | 4 000 | 634 000 |  | 3 bar, 134 °C |
|  | 2 | Steam generator 2 (reserve) | Oil | 3 500 |  | 0 |  |
|  | 3 | Hot water generator | Oil | 350 | 66 000 | 1 240 | 70 °C |
|  | 4 |  |  |  |  |  |  |

|  | No. | Name | Power (kWelectric) | Power (kWthermal) | Electr. consump. in kWh | Operating hours per year | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cooling | 1 | NH3-Unit | 190 | 596 |  | 6 482 |  |
|  | 2 | R22-Unit | 55 | 181 |  | 7 021 |  |
|  | 3 |  |  |  |  |  |  |

|  | No. | Name – use | Power (kWthermal) | Operating hours per year | Consumption (power x hours, kWh) | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Heat consumers | 1 | Pasteurization bottled beer | 38 | 3 750 | 142 500 |  |
|  | 2 | Pasteurization canned beer | 16 | 3 750 | 60 000 |  |
|  | 3 | Bottle washer | 300 | 4 000 | 1 200 000 |  |
|  | 4 | Brewing process | 690 | 4 860 | 3 354 000 |  |
|  | 5 | Heat exchanger hot water | 286 | 6 200 | 1 773 200 |  |
|  | 6 |  |  |  |  |  |
|  |  | Total: Percentage of total consumption: | 1 330 |  | 6 529 700 78.4% |  |

Worksheet 4-4: Electric consumers

Company: Cheers Beers Ltd	Period: 2002

| No. | Consumer – use | Year of constr. | Power in kW | Operating hours per year | Consumption (kWh/y) | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Chiller – NH3 units | 1984 | 190 | 6 482 | 1 231 580 |  |
| 2 | Chiller – R22 units | 1990 | 55 | 7 021 | 386 155 |  |
| 3 | Vapour compressor – brewing process | 1992 | 95 | 820 | 77 900 |  |
| 4 | CO2 plant | 1990 | 52 | 808 | 42 000 |  |
| 5 | Lighting |  | 56 | 2 400 | 134 400 |  |
| 6 | Filling line | 1998 | 80 | 4 180 | 332 580 |  |
| 7 | Brewing house | 1992 | 35 | 5 200 | 184 000 |  |
| 8 | Air compressor | 1985 | 35 | 4 000 | 140 000 |  |
| 9 | Oil furnace | 1989 | 15 | 3 950 | 59 200 |  |
| 10 |  |  |  |  |  |  |
|  | Total: Percentage of total consumption: |  | 613 |  | 2 387 815 74.2% |  |

Worksheet 4-5: Heat losses

Company: Cheers Beers Ltd	Period: 2002

Exhaust gases, wastewater, etc.

| Name of the heat flow | Flow rate | Temperature | Notes |
| --- | --- | --- | --- |
|  | [m³/h] | [m³/y] |  |  |
| Flue gas steam generator 1 | 5 380 | 8 520 960 | 210 °C | 4 MW |
| Flue gas hot water generator 1 | 470 | 877 040 | 160 °C | 350 kW |
| Wastewater bottle washer |  |  | 24 °C | Existing heat exchanger preheats fresh water. |
| Wastewater brewing house |  |  | 20 °C | Heat recovery already operating |
| Box washer |  |  | 20 °C | Not usable |

Chilling units, cooling units, etc.

| Name of the unit | Heating power | Temperature | Notes |
| --- | --- | --- | --- |
| Oil cooler, air compressor | Approx. 25 – 30 kW | 50 °C | Possible use for preheating hot water |
| Condensers, chilling units (NH3, R22) | Approx. 1 000 kW | 30 °C | Back-cooling with cooling tower |

Worksheet 4-6: Energy saving options

Company: Cheers Beers Ltd

| Option | Expected savings | Date | Responsible |
| --- | --- | --- | --- |
| Installation of a vapour compressor unit in the brewing process, oil partly substituted by electricity | 0.4 kg/hl beer | 1998 | Mr. Steam |
| Future: |  |  |  |
| Heat recovery from the air compressor to preheat hot water | 75 000 kWh or 7 500 l of oil per year | 2003 | Mr. Steam |
| Solar collector for hot water production | 13 500 kWh or 1 350 l of oil | 2004 | Mr. Steam |
| Petrol-powered vehicles partly substituted by bio-diesel vehicles | Up to 10% of fuel Approx. 20 000 l per year | 2004 – 2005 | Mr. Steam |
| ..... |  |  |  |

## Empty worksheets

# Worksheet 4-1: Energy data

Company:	Responsible:		Page:

Reference values:	Product:		Heated area:

Mileage:		..........................:

| No. | Energy | Annual consumption | Unit | Spec. costs | Conversion into kWh | Consumption in kWh | Share in % | Specific consumption | Unit |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Electricity |  | kWh | 0.10 |  |  |  |  |  |
|  | Peak load |  | kW | 135.00 |  |  |  |  |  |
| 2 | District heating |  | GJ |  | x 277.8 |  |  |  |  |
|  | Peak load |  | kW |  |  |  |  |  |  |
| 3 | Oil |  | kg | 0.50 | x 11.4 |  |  |  |  |
| 4 | Gas |  | Nm³ |  | x 10.0 |  |  |  |  |
| 5 | ………… |  |  |  |  |  |  |  |  |
| 6 | …………. |  |  |  |  |  |  |  |  |
| 7 | ……….… |  |  |  |  |  |  |  |  |
| 8 | Fuels: Diesel |  | litre | 0.80 | x 10.0 |  |  |  |  |
| 9 | Gasoline |  | litre |  | x 9.0 |  |  |  |  |
| 10 | …………. |  |  |  |  |  |  |  |  |
|  | Total |  |  |  |  |  | 100% |  |  |

Worksheet 4-2: Meters and measuring instruments

Company:

| Energy flow measured | Type of measurement and place | Meter no. | Current recording frequency | Recorded by: | Future recording frequency |
| --- | --- | --- | --- | --- | --- |

Worksheet 4-3: Conversion units and heat consumers

Company: 	Period:

|  | No. | Name | Energy carrier | Power (kWthermal) | Consumption in | Operating hours per year | Parameter (p,T) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Heat | 1 |  |  |  |  |  |  |
|  | 2 |  |  |  |  |  |  |
|  | 3 |  |  |  |  |  |  |
|  | 4 |  |  |  |  |  |  |

|  | No. | Name | Power (kWelectric) | Power (kWthermal) | Electr. consump. in kWh | Operating hours per year | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Cooling | 1 |  |  |  |  |  |  |
|  | 2 |  |  |  |  |  |  |
|  | 3 |  |  |  |  |  |  |

|  | No. | Name – use | Power (kWthermal) | Operating hours per year | Consumption (power x hours, kWh) | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| Heat consumers | 1 |  |  |  |  |  |
|  | 2 |  |  |  |  |  |
|  | 3 |  |  |  |  |  |
|  | 4 |  |  |  |  |  |
|  | 5 |  |  |  |  |  |
|  | 6 |  |  |  |  |  |
|  |  | Total: Percentage of total consumption: |  |  |  |  |

Worksheet 4-4: Electric consumers

Company:	Period:

| No. | Consumer – use | Year of constr. | Power in kW | Operating hours per year | Consumption (kWh/y) | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |
|  | Total: Percentage of total consumption: |  |  |  |  |  |

Worksheet 4-5: Heat losses

Company:	Period:

Exhaust gases, wastewater, etc.

| Name of the heat flow | Flow rate | Temperature | Notes |
| --- | --- | --- | --- |
|  | [m³/h] | [m³/y] |  |  |

Chilling units, cooling units, etc.

| Name of the unit | Heating power | Temperature | Notes |
| --- | --- | --- | --- |

Worksheet 4-6: Energy saving options

Company:

| Option | Expected savings | Date | Responsible |
| --- | --- | --- | --- |

# Footnotes

Other energy carrier such as: coal, liquid gas, wood, pellets, solar energy, etc.

Other energy carrier such as: coal, liquid gas, wood, pellets, solar energy, etc.

# Text boxes

## Example worksheets